## Slide 1: ENGI 301 Weather, News, and SMS Updates: All in One Place Proposal
10/20/19 – revised 10/24/19
Irene Kwon

## Slide 2: Background Information
Weather, news, and texts updater/viewer
  Want to have an LCD screen that displays:
    Weather (high and low of day)
    News (headlines)
    Texts received from phone (SMS)
To connect to the wifi, we connect using a wifi dongle:
    https://www.hackster.io/beaglefriends-octavosystems/pocketbeagle-alexa-0425b6
    https://www.hackster.io/logan-baldridge/spotify-pod-streaming-music-to-the-pocketbeagle-57a180
Existing technology:
    https://www.hackster.io/johnjones4/dresser-top-dashboard-913ed3
    Originally for Raspberry Pi
    Libraries: Pillow (has different widgets)
    Improvement on this: want to receive/display SMS texts on phone
Existing dashboard for news (but uses Raspberry Pi)

## Slide 3: User Interface
Buttons
  To press through all the different updates
  Two buttons
    One for powering off
    One for pressing through the different updates
LCD Screen
Power On
Scroll Through
*Rough idea of hardware aspect of device

## Slide 4: System Block Diagram
USBA Female Breakout
LCD Screen
Wifi/Bluetooth Dongle
PocketBeagle
USB1
SPI
Power Bank
4.8A
Button
Button
GPIO
GPIO

## Slide 5: Power Block Diagram
USBA Female Breakout
LCD Screen
Wifi/Bluetooth Dongle
PocketBeagle
VIN_USB1
3.3V P1_14
Power Bank
4.8A
5V
3.3V
Button
Button
GPIO 59
GPIO 58
3.3V
3.3V

## Slide 6: Components / Budget
Component | Need to Buy | Cost
PocketBeagle | No | $25
SD Card | No | $8
Edimax USB Wifi Dongle | No | $15
Adafruit 2.2" Color TFT LCD | Yes | $20
INIU Portable Charger, 10000mAh Power Bank, 4.8A High-Speed | Yes | $20
INISparkFun USB Type A Female Breakout (2, 15 kohm pull-down resistors may be needed U Portable Charger, 10000mAh Power Bank, 4.8A High-Speed | No | $4.50
Cylewet 25Pcs 12x12x7.3mm Momentary Tact Tactile Push Button Switch Touch Switch Micro Switch 4 Pins SMD PCB with Cap for Arduino (Pack of 25) CYT1009 *but only need 2 buttons | Maybe | $7.89